## Slide 1
Apopka, FL – May 2008
Results of Advanced Irrigation
Controller Testing on Vegetables
Lincoln Zotarelli, Ph.D.
Michael D. Dukes, Ph.D., P.E.
University of Florida
IFAS -Institute of Food and Agriculture Sciences
Agricultural & Biological Eng. Dept
Manatee County Grower Workshop

## Slide 2
Introduction
Production challenges in Florida
High Temperature  Water demand  Supplemental Irrigation
SANDY SOILS
      Excessively well-drained
      Low soil organic matter
      Low water and nutrient holding capacity
      High application of water and nutrients

## Slide 3
Introduction
High vertical water movement
Low lateral soil water movement
High susceptibility to NO3-N leaching
Higher requirement
of fertilizer
direct effect on
production costs &
vegetable yield

## Slide 4
Conventional irrigation management: inadequate to ensure optimal resource use and to minimize nutrient leaching
Use of technological innovations can:
  enhance production efficiency
  provide local growers with a competitive edge
  reduce environmental impacts
Research priorities: Lack of precise information on crop water & nutrient status  excessive water & fertilizer use
Introduction

## Slide 5: Goal: Enhancing fertilizer use efficiency Strategy: Improve water & N retention in the root zone Implementation:  Proper rate & application of N-fertilizer  Use of soil moisture sensor based systems  Use of subsurface drip irrigation on tomatoes  Use of twin drip lines on peppers
Conceptualize research strategies

## Slide 6
Actual soil moisture and irrigation on sandy soils
Saturation
Field Capacity
Wilting Point
VWC > 30%
-1 cbar
-0.001 MPa
VWC approx. 10-12%
-10 cbar
-0.01 MPa
VWC approx. 6%
-1500 cbar
-1.5 MPa
Soil Moisture Sensor can also translate soil moisture to voltage!
e.g. 525 mV 430 mV 320 mV

## Slide 7: Soil moisture sensors and automated irrigation
SMS
miliVolts
540 mV
500 mV
430 mV
340 mV
300 mV
Ideal
soil moisture to:
1. Maximize yield
2. Minimize irrigation water application
3. Reduce N-leaching

## Slide 8: Soil moisture sensors and automated irrigation
Soil moisture probe
2. Controller
3. Timer
Solenoid valve
on/off

## Slide 9: Soil moisture sensors and automated irrigation
Controller
Soil Moisture
Sensor
Timer
Solenoid valve
Flowmeters
Pressure regulator
Filter

## Slide 10
Sensor Based Irrigation Control

## Slide 11: Local: Plant Science Research and Education Unit Citra, Marion Co., FL Sandy soil, organic matter below 1% Crops: Spring Tomato (3yr) – “Florida 47” Spring (4yr) and Fall (2 yr) - Green Bell Pepper “Brigadier” Fall Zucchini (2yr) – “Wild Cat”
Experimental Field

## Slide 12: Field Preparation / Mulching / Fumigation / Transplanting

## Slide 13
Experimental Field - Irrigation Treatments
10% VWC - SINGLE DRIP IRRIGATION
irrigation 5 possible windows of 24 min
depending of the VWC
10% VWC – SDI, subsurface drip irrigation
irrigation 5 possible windows of 24 min
depending of the VWC
3. TIME FIXED – 2h of continuous irrigation
(approx. 0.2 in/day)
Tomato
Soil moisture sensor threshold

## Slide 14
Tomato Bed System – Subsurface Drip Irrigation
0-6 inches
6-12 inches
12 – 24 inches
24 – 36 inches
Fertigation Drip
Fertigation Wet Zone “Bulb”
Irrigation Wet Zone “Bulb”
Soil Depth Layers
Irrigation Drip

## Slide 15: Tomato: Yield & Irr. Use Efficiency
 | Irrigation |  |  | Water | Marketable Yield |  |  | Irr Water Use
Treatment | inches |  | gal/100 ft | Saved | 1000 lb/acre | 25lb Box/acre |  | Efficiency lb/100 gal
Spring 2006 |  |  |  |  |  |  |  | 
SM sensor |  | 7.3 | 2,965 | 47% | 133 a | 2144 a |  | 26 a
SDI |  | 10.8 | 3,984 | 29% | 127 a | 2052 a |  | 17 b
Fixed Time |  | 15.4 | 5,665 | 0% | 106 b | 1706 b |  | 10 c
Spring 2007 |  |  |  |  |  |  |  | 
SM sensor |  | 8.9 | 3,289 | 40% | 189 a | 3058 a |  | 31 a
SDI |  | 13.9 | 5,143 | 7% | 174 a | 2815 a |  | 18 b
Fixed Time |  | 15.0 | 5,506 | 0% | 156 b | 2530 b |  | 15 c

## Slide 16: Tomato: Yield & N-rate
Chart: Tomato Yield (boxes/acre)
| Spring 2006 | Spring 2007
160 lb/ac | 1913 | 2601
200 lb/ac | 1877 | 2951
300 lb/ac | 2116 | 2851
N-fertilizer
Calcium nitrate
a
a
a
a
a
a

## Slide 17: Tomato: water percolation and nitrate leaching
Chart: Nitrate Leaching
| SMS | SDI | Fixed Time
160 lb/ac | 19
200 lb/ac | 2.5 | 3.5 | 20
300 lb/ac | 11 | 12 | 43
Chart: Percolation of irrigation water in the lysimeters
| Irrigation Treatments
SMS | 0.2
SDI | 0.4
Fixed Time | 2
d
b
a
a
b
b
c
c

## Slide 18
24 hrs
3 days
7 days
Effect of irrigation on solute displacement
(injecting dye in fertigation lines)
soil sensor based
irrigation
fixed time irrigation schedule
16in
+38 in

## Slide 19
SDI
SMS
Fixed
time
Tomato
78%
66%
51%
13%
22%
28%
9%
12%
21%
6 in
12 in
36 in
Root length density (cm cm-3)

## Slide 20
Experimental Field - Irrigation Treatments
4% VWC - irrigation 5 possible windows of 24 min
depending of the VWC (only Spring 08)
2. 8% VWC - “
3. 10% VWC - “
4. 12% VWC - “
5. TIME FIXED – 2h of continuous irrigation (~ 0.2 in/day)
Green Bell Pepper
Soil moisture sensor threshold

## Slide 21: Pepper: Yield & Irr. Use Efficiency
 |  | Irrigation |  | Water |  | Marketable Yield |  |  | Irr Water Use
Treatment |  | inches | gal/100 ft | Savings |  | 1000 lb/acre | 30lb Box/acre |  | Efficiency lb/100 gal
Spring 2007 |  |  |  |  |  |  |  |  | 
SMS 8% | 6.5 |  | 2,376 | 50% |  | 26.3 a | 877 a |  | 15 a
SMS 10% | 7.0 |  | 2,594 | 45% |  | 24.3 a | 811 a |  | 13 a
SMS 12% | 10.4 |  | 3,825 | 18% |  | 20.5 a | 684 a |  | 8 b
Fixed Time | 12.6 |  | 4,637 | 0% |  | 22.8 a | 761 a |  | 6 b

## Slide 22: Pepper: Yield & N-rate
Chart: Yield (30 lb box/ac)
| Spring 2007 | Fall 2007
160 lb/ac | 737 | 1344
200 lb/ac | 791 | 1379
300 lb/ac | 832 | 1305
N-fertilizer
Calcium nitrate
a
a
a
a
a
a
N-rate (lb of N/ac) of calcium nitrate

## Slide 23: Pepper: water percolation and nitrate leaching
Chart: Nitrate Leaching
| SMS 10% | SMS 12% | Fixed Time
200 lb/ac | 14 | 29 | 37
300 lb/ac | 18 | 36 | 42
Chart: Percolation of irrigation water in the lysimeters
| Irrigation Treatments
SMS 10% | 0.6
SMS 12% | 1.3
Fixed Time | 1.7
b
ab
a
a
b
c
ab
c
c

## Slide 24
Application uniformity
drip tape at
center of the bed
dry soil
at side of the bed
wet soil
Photo: L. Zotarelli
TWIN DRIP LINES
Soil moisture after 1 hour of irrigation

## Slide 25: Pepper: Yield & Irr. Use Efficiency Spring 2008
 |  | Irrigation |  | Water | Marketable Yield |  |  | IWUE
Treatment |  | inches | gal/100 ft | Saving | 1000 lb/acre | 30lb Box/acre |  | lb/100 gal
Single Drip |  |  |  |  |  |  |  | 
SMS 4% |  | 3.2 | 1,174 | 76% | 23.5 c | 795 d |  | 27.2 a
SMS 8% |  | 4.6 | 1,710 | 65% | 27.4 b | 913 c |  | 21.7 b
SMS 12% |  | 5.4 | 2,000 | 60% | 31.9 b | 1,064 b |  | 21.5 b
Fixed Time 2h |  | 13.4 | 4,941 | 0% | 29.4 b | 981 b |  | 8.1 c
F. Time 4x24 min |  | 10.2 | 3.767 | 23% | 36.2 a | 1,207 a |  | 15.6 b
Twin Drip |  |  |  |  |  |  |  | 
SMS 8% |  | 4.4 | 1,623 | 67% | 27.0 b | 901 c |  | 22.5 b
SMS 12% |  | 7.9 | 2,912 | 41% | 37.4 a | 1,249 a |  | 17.4 b
Single N-rate of 200 lb/ac

## Slide 26: PROJECT: Evaluation and Demonstration of Soil Moisture Based On-demand Irrigation Controllers for Vegetable Production (SWFWMD B228)

## Slide 27: PROJECT: Evaluation and Demonstration of Soil Moisture Based On-demand Irrigation Controllers for Vegetable Production (SWFWMD B228)
Soil: Spodosol
Slope: <2%
Water table: 20-36 inches
Pepper variety: HM2641
Transplanting: Sep 15 2008

## Slide 28: PROJECT: Evaluation and Demonstration of Soil Moisture Based On-demand Irrigation Controllers for Vegetable Production
Sensor# 1
8-14 inches
2-6 inches
Sensor# 3
Sensor# 2
Sensor# 4
Raised bed
Acclima Data
Recorder
Antenna

## Slide 29: PROJECT: Evaluation and Demonstration of Soil Moisture Based On-demand Irrigation Controllers for Vegetable Production

## Slide 30: PROJECT: Evaluation and Demonstration of Soil Moisture Based On-demand Irrigation Controllers for Vegetable Production (SWFWMD B228)
N
Flush valves
Sensor Data recorder (Acclima SD12)
Manifold and drip
Manifold
Zone 4 5 6
A
B
D
C
980 ft
2,170 ft
Drip Lines
Aprox. 41 acres
Photo source: Web Soil Survey, NRCS. http://websoilsurvey.nrcs.usda.gov/app/.

## Slide 31: PROJECT: Evaluation and Demonstration of Soil Moisture Based On-demand Irrigation Controllers for Vegetable Production
Chart: A-Soil moisture
Chart: B-Soil moisture
Chart: C-Soil moisture
Chart: D-Soil moisture

## Slide 32
Sensor-based irrigation systems increased water use efficiency and yield for tomato and pepper
Conclusions
Application of N rates in excess of 200 lb/ac (IFAS recommendation) did not increase yield with rigorous control of the irrigation
Combination of high irrigation rates with high N rates greatly increased nitrate leaching
Subsurface drip irrigation (tomato) can be an efficient option to reduce N leaching maintaining yields
Twin drip (pepper) offer a better water distribution in the bed which may result in higher yields

## Slide 33
Evaluation of research plot practices (e.g. SMS irrigation, small frequent irrigation events) at field scale
Development of scheduling recommendations
Detailed analysis of sensor positioning in plastic mulched beds and minimum number of sensors per area
Use of electrical conductivity to track fertilizer movement in the soil
Use of wireless communication between soil moisture sensors and irrigation controllers
Future Research

## Slide 34
Thanks!
Acknowledgements:
Research supported by Southwest Florida Water Management District (B228) and Florida Dept. of Agric. and Consumer Serv. Project FDACS # 9189.
We’d like to thank the staff at the PSREU research facility in Citra, FL, Buck Nelson, Larry Miller, Danny Burch, Andy Schreffler, for their assistance with field operations.
Questions?